## Slide 1: LHC OPN and LHC ONE
”LHC networks”
Marco Marletta (GARR) – Stefano Zani (INFN CNAF)

## Slide 2: TIERs and data movement
T0 (CERN) Where data are generated
T1 (11 Sites all over the world) are the first level of data distribution in charge of safe keeping, sharing of data and reconstruction (not all data are replicated in every TIER1).
T2 (more than 140 sites all over the world) are sites more specifically dedicated to data analysis activity.
T3 (many hundreds) are little centers in charge of interactive analysis activity.

## Slide 3: Main traffic flows
A) T0-T1 and T1-T1 (LHCOPN) IN PLACE AND STABLE
In order to address this type of traffic It has been created an Optical Private Network connecting CERN and the 11 National TIER1s (LHC-OPN)
B) T1-T2 and T2-T2 (LHCONE) IN IMPLEMENTATION PHASE
In the original design of data movements between tiers named MONARC each T2 was supposed to transfer data only from its national T1.
Last year experiments changed their computing model assuming each T2 could have access to data stored potentially in every T1 and also in any T2! To address this type of traffic a new network named LHC Open Network Environment (LHCONE) is in phase of implementation.

## Slide 5: LHCONE General Concepts
LHCONE will implement different services:
Multipoint Connection Service (Entering in production PHASE)
Point to Point Service
  Static (Production technology available)
  Dynamic (R&D)
Aggregation
Network
Aggregation
Network
Aggregation
Network
Aggregation
Network
T2
T1
T2
T2
T1
T2
T2
LHCONE
continent
continent
continent
T2
T2
distributed exchange point
single node exchange point
Any site connecting this network is generally named connector and could access LHCONE through its National Research Education Network or directly through an Exchange Point participating in LHCONE (Starlight, ManLan, NetherLight, CernLight, WIX).

## Slide 6
Multipoint Connection Service is an L3 VPN network based on routers and VRFs (Virtual Routing & Forwarding) instances.
For connectors works like a dedicated IP routed network.
This is the model of the current “Production” LHCONE implementation.
LHCONE Multipoint Connection Service

## Slide 7
ESnet
USA
Chicago
New York
BNL-T1
Internet2
USA
Harvard
CANARIE
Canada
UVic
SimFraU
TRIUMF-T1
UAlb
UTor
McGilU
Seattle
TWAREN
Taiwan
NCU
NTU
ASGC
Taiwan
ASGC-T1
KERONET2
Korea
KNU
LHCONE VPN domain
End sites – LHC Tier 2 or Tier 3 unless indicated as Tier 1
Regional R&E communication nexus
Data communication links, 10, 20, and 30 Gb/s
See http://lhcone.net for details.
NTU
Chicago
LHCONE: A global infrastructure for the LHC Tier1 data center – Tier 2 analysis center connectivity
NORDUnet
Nordic
NDGF-T1a
NDGF-T1a
NDGF-T1c
DFN
Germany
DESY
GSI
DE-KIT-T1
GARR
Italy
INFN-Nap
CNAF-T1
RedIRIS
Spain
PIC-T1
SARA
Netherlands
NIKHEF-T1
RENATER
France
GRIF-IN2P3
Washington
CUDI
Mexico
UNAM
CC-IN2P3-T1
Sub-IN2P3
CEA
CERN
Geneva
CERN-T1
SLAC
GLakes
NE
MidW
SoW
Geneva
KISTI
Korea
TIFR
India
India
Korea
FNAL-T1
MIT
Caltech
UFlorida
UNeb
PurU
UCSD
UWisc
UltraLight
UMich
Amsterdam
GÉANT
Europe

## Slide 8
Point to Point service (R&D)
The basic idea is to provide a sheduled circuit on demand service to the LHC community.
Point-to-point circuit service should have
  guaranteed bandwidth
  Predictable delay
  No jitter
Scheduled in advance
Intrinsically non-redundant
Can be either
  Static (setup and don’t tear down for months or years)
  Dynamic (setup on demand, tear down as soon as it is not needed)
Application driven “circuit” creation
  A meeting with People from Experiments (Middleware developers) will be scheduled to understand if it is possible to integrate in the middleware and end to end circuit creation.
The goal is to find a possible production solution for the 2014

## Slide 9: Point to Point service (R&D)
The main technologies for SDN (Software Defined Networks) used by network operators are:
DICE1 IDCP (Inter Domain Controller Protocol) Solutions.
  ESnet OSCARS (On-demand Secure Circuits and Advance Reservation System)
  Internet2 ION (Interoperable Ondemand Network)
  GEANT AutoBAHN In europe
OGF NSI (Network Service Interface) is an effort to standardize the P2P services deployed by NRENs.
  OpenFlow: To build an end to end software defined network is essential to make the control plane to interact with Switch/Router devices and OpenFlow protocol is starting to be supported by many different switch/router manufacturer like Cisco, IBM (Blade Networks), DELL (Force10) and Brocade. There is an LHCONE Working group in charge of building a pilot based on the OpenFlow
1 (Dante, Internet2, CANARIE, and Esnet)

## Slide 10: Monitoring
perfSONAR-MDM and perfSONAR-PS are the end to end tools currently in use in LHCOPN and LHCONE communities for Bandwidth and latency measurement.
perfSONAR-MDM (Hardware solution owned and managed by DANTE). In place in TIER1’s sites.
perfSONAR-PS (Software deployed on servers owned by sites): New DASHBOARDS based on perfSONAR-PS data are in development for LHCOPN and in a subset of ATLAS TIER2s as a pilot monitoring system for LHCONE.
perfSONAR-PS Toolkit Page: http://psps.perfsonar.net/toolkit/
Tom’s Dashboard: https://130.199.185.78:8443/exda/?page=25&cloudName=LHCOPN
perfSONAR-MDM (Multi Domain Monitoring) Toolkit Page: http://www.geant.net/service/perfsonar/pages/home.aspx

## Slide 11: Why LHCONE?
Better management of the LHC traffic on the national and international paths
  Using a VPN it is possible to engineer LHC traffic
Use of dedicated LHCONE network resources
  GEANT will install a new transatlantic 10 Gb/s link Geneva – Starlight (Chicago) (Before the end of June 2012)
  GARR-X will install dedicated capacity between GARR PoPs with T2 and Bologna

## Slide 12: Transition to LHCONE network in Italy
…
T1
T1
GARR
General IP
Backbone
NA
T2
RM
T2
PI
T2
LNL
T2
MI
T2
CNAF
T1
T1
CERN
T0
LNF
T2
2x1Gb/s
10Gb/s
1Gb/s
1Gb/s
2x10Gb/s OPN
Via GARR
1Gb/s
1Gb/s
2x1Gb/s
2x1Gb/s
3x1Gb/s
T1
T1
T1
T1
T1
T1
T1
DE-KIT
LHCOPN
T0-T1
T1-T1
T1-T2 General IP
1Gb/s
GEANT
3x10Gb/s
BA
T2
CT
T2
TO
T2
GARR
LHC-ONE
VRF
RM
T2
NA
T2
BA
T2
GEANT
LHCONE
VRF
T1-T2 LHCONE
MI
T2
PI
T2
1x10Gb/s OPN
Via GARR

## Slide 13: LHCONE site access
A is the main site («Sezione» or «laboratorio»)
A’ is the T2 or the «GRID farm»
Three different cases
  1 – A and A’ have separate routers
  2 – A and A’ have separate routers but A’ can’t do BGP
  3 – A and A’ share the same router
A
Site
A’
R&E IP
LHCONE

## Slide 14: 1 – A and A’ have separate routers
GEANT
GEANT LHCONE routing instance
GARR LHCONE routing instance
GARR IP service
LAN Tier2
LAN Sezione
Routing statico o dinamico
Routing BGP
Accesso Tier2: 10GE in GARR-X
Accesso Sezione INFN: 1 x GE in GARR-X
Backup link
Dedicated LHCONE link
T2 general purpose link
Can be a single physical link with VLAN trunk

## Slide 15: 2 - A and A’ have separate routers but A’ can’t do BGP
GEANT
GEANT LHCONE routing instance
GARR LHCONE routing instance
GARR IP service
LAN Tier2
LAN Sezione
Routing statico o dinamico
Routing statico
Accesso Tier2: 10GE in GARR-X
Accesso Sezione INFN: 1 x GE in GARR-X
Backup link
LHCONE +
General purpose link
Interconnection between instances

## Slide 16: 3 - A and A’ share the same router
GEANT
GEANT LHCONE routing instance
GARR LHCONE routing instance
GARR IP service
LAN Tier2
LAN Sezione
Routing statico
Routing statico
Interconnection between instances
Accesso Tier2: 10GE in GARR-X
Accesso Sezione INFN: 1 x GE in GARR-X
Source-based routing

## Slide 17: Adding a new connection can cause problems
Asymmetric routing and stateful firewalls are natural enemies
If BGP routing is done by GARR (cases 2 and 3) you are safe (!)
If BGP routing is done by you (case 1) you can either
  avoid using firewalls (LHCONE is a circle of trust)
  Or take care asymmetric routing is not in place
Connection Recommendations to address Asymmetric Routing (Quoting Mike O’Connor - ES-NET)
Define local LAN address ranges that will participate in LHCONE. Advertise these address range prefixes to LHCONE using BGP.
Agree to accept all BGP route prefixes advertised by the LHCONE community.
Ensure that the LHCONE defined ranges are preferred over general R&E IP paths.
Avoid static configuration of packet filters, BGP prefix lists and policy based routing, where possible.

## Slide 18: LHCONE in Italy
Sede | Network | Joined LHCONE
CNAF Bologna (T1) | 131.154.128.0/17 | 26 oct 2011
Bari (T2) | 212.189.205.0/24 90.147.66.0/24 | 26 apr 2012
Catania (T2) | 192.84.151.0/24 | Not yet
Frascati (T2) | 192.84.128.0/25 | Not yet
Legnaro (T2) | 192.135.30.0/27 192.135.30.192/27 | Not yet
Napoli (T2) | 90.147.67.0/24 | 01 dic 2011
Milano (T2) | 192.135.14.0/24 | 10 may 2012
Pisa (T2) | 192.135.9.0/24 193.205.76.0/23 | 10 may 2012
Roma1 (T2) | 141.108.35.0/24 (LHC Services) 141.108.36.0/23 (CMS) 141.108.38.0/23 (ATLAS) | 07 may 2012
Torino (T2) | 193.206.184.0/26 193.205.66.128/25 | Not yet

## Slide 19: Traffic monitoring
CNAF
Napoli
Bari, Pisa, Milano, Roma1

## Slide 20: Aggregate GEANT traffic

## Slide 21
Ge1
Ss
An
Ve
Tn
Pv
Cz
Le
Mt
Pz
Cs
Sa
Me
Fra
Pg
Aq1
Mi2
Fi1
Mi1
Bo1
RM2
Mi1
To1
Pi1
Bo3
Bo1
Pd2
Ts1
Mi3
Na1
Ct1
RM2
Rm1
BB20
BB19
BB21
BB22
BB24
BB27
BB26
BB35
BB17
BB14
BB34
BB33
BB32
BB10
C37-C38-C39-C40
BB15
BB28
Pv1
C33-C34-C35-C36
BB4-2
C2-C3
C49-C50
C47-C48
C23
C20
C21
BB29
C1
C4-C5
C6+UP2
C9
C41-C42-C43-C44
C51-C52
C7
C8
C13
C14
C16
C10
C18
C45-C46
C29-C30-C31-C32
C12
C11+UP1
C17+UP3
C19/TEMP
C22
C24
da ord.
RMT
A7T1
A7T3
A7T2
8x10G
8x10G
8x10G
8x10G
Fe
Pa1
BB31
BB4-1+C15
Ca1
Mi2
Br
Ba1
BB16
C26
C27
BB30*
RM1
* - BB30 is landing in RM1, and will be extended up to RM2
Mi2
Mi1
Bo1
RM2
Ba1
Na1
Mi3
Ct1
Pd2
Ca1
Pa1
Tn
Ve
Ge1
Fra
Ss
Aq1
Pg
Br
Le
Mt
Pz
Sa
Me
Cz
Cs
An
Fe
GARR-X Network layout
RM1

## Slide 22: Infrastruttura Router+Switch
Bo1
INFN-Roma1
INFN-Bari
INFN-Napoli
INFN-Catania
INFN-Milano
INFN-LNL
INFN-Torino
INFN-Pisa
INFN-LNF
INFN-CNAF Tier1
Fi1
Pa1
Mi1
Ca1
To1
Pi1
Mi2
Bo3
Bo1
Pd2
Ts1
Mi3
Na1
Ba1
Ct1
RM2
Rm1
INFN-Tier2 |  | 
1 | Milano | Mi3Bo1
2 | Roma | Rm2 Bo1
3 | Legnaro | Pd2 Bo1
4 | Catania | Ct1 Bo1
5 | Napoli | Na1 Bo1
6 | Pisa | Pi1 Bo1
7 | Frascati | Rm1 Bo1
8 | Torino | To1 Bo1
9 | Bari | Ba1 Bo1
10 | CNAF | 4*10G
Aggregation Node |  |  | 
1 | A | Ba1 | Bari-Amendola
2 | A | Bo3 | Bologna-Gobetti
3 | A | Ca1 | Cagliari-Marengo
4 | A | Cti1 | Catania-Cittadella
5 | A | Fi1 | Firenze-Sesto
6 | A | Mi3 | Milano-Colombo
7 | A | Na1 | Napoli-Mt.S.Angelo
8 | A | Pa1 | Palermo-Scienze
9 | A | Pd2 | Padova-Spagna
10 | A | Pi1 | Pisa-S.Maria
11 | A | Rm1 | Roma-Sapienza
12 | A | To1 | Torino-Giuria
13 | A | Ts1 | Trieste-Valerio
Bo1
INFN-Roma1
INFN-Bari
INFN-Napoli
INFN-Catania
INFN-Milano
INFN-LNL
INFN-Torino
INFN-Pisa
INFN-LNF
INFN-CNAF Tier1
GEANT LHCONE
LHCOPN
RM2
Mi2
Mi1

## Slide 23: Italian Tier2 in GARR-X
Bo1
INFN-Roma1
INFN-Bari
INFN-Napoli
INFN-Catania
INFN-Milano
INFN-LNL
INFN-Torino
INFN-Pisa
INFN-LNF
INFN-CNAF Tier1
To1
Pi1
Pd2
Na1
Ba1
Ct1
Rm1
Mi3
RM2
R
LHCONE
LHCOPN

## Slide 24
GEANT LHCONE
Ct1
INFN-CNAF Tier1
LHCOPN
INFN-Catania
Infrastruttura Router+Switch
Mi1
Mi2
Bo1
RM2
Bo1
RM2
Mi2
Mi1

## Slide 25
RM2
Bo1
INFN-CNAF Tier1
GEANT LHCONE
INFN-Catania
Ct1
General purpose links
LHCONE dedicated link
LHCONE link will be chosen using MPLS traffic engineering
Backup via GP will be provided at lower capacity

## Slide 26
The End..
Thank You for your attention!

## Slide 27: Backup Slides

## Slide 28: Plot of general Transatlantic Connectivity

## Slide 29: Some numbers on LHC OPN Connections
Globabl T0-T1s
INFN CNAF TIER1 T0-T1+T1-T1